## Slide 1: Portable Grid Square LCD Bill Pence KI4US

## Slide 2: Grid Square LCD Display
  Simple, portable, stand alone low cost Grid Square LCD display hardware
    Arduino of about any flavor
    I2C LCD
    GPS module
    7 Arduino jumpers, or can be soldered with hook up wire as desired.
  Can be powered in several ways
    Battery connected to Arduino DC input
    Portable USB battery
    Direct 12v from power point in vehicle to Arduino DC input

## Slide 3: Grid Square LCD Display
LCD showing 6 digit grid square, number of satellites used for fix, and current Latitude/Longitude.
The sketch has can be customized for LCD display content and format to show time, Lat/Long, grid, etc.

## Slide 4: Wiring info

## Slide 5: Components info and Sketch location
Parts easily obtained at Amazon.
GPS module
https://www.amazon.com/gp/product/B01D1D0F5M
I2C LCD module
https://www.amazon.com/GeeekPi-Character-Backlight-Raspberry-Electrical/dp/B07S7PJYM6
Arduino Uno Compatible module
https://www.amazon.com/ELEGOO-Board-ATmega328P-ATMEGA16U2-Compliant/dp/B01EWOE0UU/
Sketch (program) available at github.com with open access
https://github.com/bpguy/gps_grid_sq_lcd

## Slide 6
Let’s talk a bit about grids….

## Slide 7
Grids are usually used as 4 or 6 digit values, but can be extended.
The extra characters add further location precision
  2 letters specify a 20° longitude x 10° latitude segment of the earth
  2 numbers refine the segment to a 2° longitude x 1° latitude sub segment
  2 letters further refine the sub segment to 5’ x 2.5’ values
  Alternating numbers and letters continue refining the location

## Slide 8: Grid Square resources
QST January 1989, pp. 29-30, 43 contains info on the grid square notation
W8BH.net has a nice document with an algorithm for computing grids from GPS coordinates located at http://w8bh.net/grid_squares.pdf
Next, an example spreadsheet that implements the w8bh notes for computing 10 digits

## Slide 10
Thanks for your interest